*******************Default*******************
Pico2_w pico-examples
04/11/25
*******************Default*******************
“git clone https://github.com/develone/pico-examples.git -b test-dev”
#!/bin/bash
#rm -rf build-2350
#mkdir build-2350
cd build-2350
cmake .. -DPICO_BOARD=pico2_w -DPICO_PLATFORM=rp2350 -DWIFI_SSID="WIFI_SSID" -DWIFI_PASSWORD="WIFI_PASSWORD"
make
The first issue in the build
CMake is dropping a preprocessor definition: WIFI_PASSWORD="xxxxxxxxx#xx"
The next tried adding
export WIFI_SSID="WIFI_SSID"
export WIFI_PASSWORD="WIFI_PASSWORD"
Modified the file
devel@pi5-90:~/pico-examples $ git diff pico_w/CMakeLists.txt
diff --git a/pico_w/CMakeLists.txt b/pico_w/CMakeLists.txt
index f66c02e..35fd59a 100644
--- a/pico_w/CMakeLists.txt
+++ b/pico_w/CMakeLists.txt
@@ -1,28 +1,9 @@
 cmake_minimum_required(VERSION 3.12)
-
-if (PICO_CYW43_SUPPORTED) # set by PICO_BOARD=pico_w
- if (NOT TARGET pico_cyw43_arch)
- message("Skipping Pico W examples as support is not available")
- else()
-
- if (DEFINED ENV{WIFI_SSID} AND (NOT WIFI_SSID))
- set(WIFI_SSID $ENV{WIFI_SSID})
- message("Using WIFI_SSID from environment ('${WIFI_SSID}')")
- endif()
-
- if (DEFINED ENV{WIFI_PASSWORD} AND (NOT WIFI_PASSWORD))
- set(WIFI_PASSWORD $ENV{WIFI_PASSWORD})
- message("Using WIFI_PASSWORD from environment")
- endif()
-
- set(WIFI_SSID "${WIFI_SSID}" CACHE INTERNAL "WiFi SSID for examples")
- set(WIFI_PASSWORD "${WIFI_PASSWORD}" CACHE INTERNAL "WiFi password for examples")
+set(WIFI_SSID $ENV{WIFI_SSID})
+set(WIFI_PASSWORD $ENV{WIFI_PASSWORD})
+message("Using WIFI_SSID from environment ('${WIFI_SSID}')")
+message("Using WIFI_PASSWORD from environment")
+message("Using WIFI_PASSWORD from environment ('${WIFI_PASSWORD}')")

        add_subdirectory(wifi)
- if (NOT TARGET pico_btstack_base)
- message("Skipping Pico W Bluetooth examples as support is not available")
- else()
        add_subdirectory(bt)
- endif()
- endif()
-endif()

xx

xx

xx

xx

xx

xx
built on pi5-80

pico-examples/build-2350/pico_w/wifi/wifi_scan/picow_wifi_scan_poll.uf2

Welcome to minicom 2.8

OPTIONS: I18n
Port /dev/ttyUSB1, 13:15:10

Press CTRL-A Z for help on special keys
Performing wifi scan
ssid: DIRECT-09-HP DeskJet 2600 series rssi: -81 chan: 1 mac: f8:b4:6a:5c:2d:0b sec: 5
ssid: ATT3TV6WQs rssi: -79 chan: 1 mac: c8:52:61:4e:d2:50 sec: 5
ssid: DIRECT-09-HP DeskJet 2600 series rssi: -79 chan: 1 mac: f8:b4:6a:5c:2d:0b sec: 5
ssid: ATT3TV6WQs rssi: -80 chan: 1 mac: c8:52:61:4e:d2:50 sec: 5
ssid: ATTXChY8YW rssi: -86 chan: 3 mac: ec:c3:02:28:d5:44 sec: 5
ssid: ATTXChY8YW rssi: -87 chan: 3 mac: ec:c3:02:28:d5:44 sec: 5
ssid: ATTXChY8YW rssi: -86 chan: 3 mac: ec:c3:02:28:d5:44 sec: 5
ssid: ATTtpHTfPi rssi: -19 chan: 4 mac: cc:ab:2c:c7:5e:54 sec: 5
ssid: ATTtpHTfPi rssi: -19 chan: 4 mac: cc:ab:2c:c7:5e:54 sec: 5
ssid: ATTtpHTfPi rssi: -21 chan: 4 mac: cc:ab:2c:c7:5e:54 sec: 5
ssid: ATT47CJH5z_EXT rssi: -61 chan: 6 mac: 3c:84:6a:46:98:f0 sec: 7
ssid: Pico_w-Net3 rssi: -54 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: Century Link rssi: -53 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: ATT47CJH5z_EXT rssi: -59 chan: 6 mac: 3c:84:6a:46:98:f0 sec: 7
ssid: Century Link rssi: -46 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: ATT47CJH5z_EXT rssi: -59 chan: 6 mac: 3c:84:6a:46:98:f0 sec: 7
ssid: Pico_w-Net3 rssi: -47 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: ATTtpHTfPi rssi: -23 chan: 4 mac: cc:ab:2c:c7:5e:54 sec: 5
ssid: Pico_w-Net3 rssi: -48 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: Century Link rssi: -46 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: Pico_w-Net3 rssi: -51 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: ATT47CJH5z_EXT rssi: -59 chan: 6 mac: 3c:84:6a:46:98:f0 sec: 7
ssid: Century Link rssi: -44 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: Pico_w-Net3 rssi: -50 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: Pico_w-Net3 rssi: -51 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: Century Link rssi: -47 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: Pico_w-Net3 rssi: -47 chan: 7 mac: dc:a6:32:09:35:24 sec: 5
ssid: Century Link rssi: -55 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5
ssid: NETGEAR38 rssi: -74 chan: 10 mac: bc:a5:11:1c:a6:85 sec: 5
ssid: Century Link rssi: -50 chan: 7 mac: dc:a6:32:27:e2:21 sec: 5